## Slide 1: Launcher

## Slide 2: 設定

## Slide 3: 平滑化と微分
Excelの入力データに対し、x,yで選んだ関数に対して多項式適合平滑化、微分を行う。
Test: 異なる条件で平滑化を行い、最適条件を確認する
データの変数 “x:” と関数値 “y:” と選択する。
“xmin:”, “xmax:” で計算する範囲を選ぶ。
平滑化条件の “model:” は、単純移動平均 (simple moving average) が多項式適合平滑化より良いことは （まず）ないので、polynomialを選ぶ
“Order of polynomial:” で多項式の次数を選ぶ。この次数、+1、+2次の平滑化をtestする。
“Number of smoothing data:” で、平滑化に使うデータ点数を選ぶ。奇数のみ。
“Increment of smoothing data for mode=test:” に、testモードでの平滑化点数の増分を入力。5.の点数に、この数と２倍の数を加えた平滑化点数をtestする。
“test”ボタンを押して実行
Plot: 最適条件で平滑化したグラフのみを表示する。
“Order of polynomial:”, “Number of smoothing data:” に最適値を入力する
“plot”ボタンで描画
微分
“Order of differentiation” で微分次数を選択。0は微分しない。 多項式の次数よりも高い微分は無意味。

## Slide 4: test
平滑化点数を11,21,31点
単純移動平均
2次多項式平滑化
5次多項式平滑化
平滑化点数を11,21,31点
平滑化点数を11,21,31点

## Slide 5: 平滑化
着目している点 N点 のある平均を取る
・ 単純移動平均 重みを均一に １/N とする
・ 加重移動平均 重み: 線形、三角形、指数関数、Gauss関数 など
・ 多項式適合法 (Savizky-Golay法)
着目している点を中心に (2m+1)点をとり、 多項式最小二乗法で中心点の値を求める
=> 実際には最小二乗法を実行する必要はない

## Slide 6: 多項式適合法 (Savizky-Golay法) の重み
南茂夫, 科学計測のための波形データ処理, CQ出版社 (1986)
(2m+1)点を用いた2,3次多項式適合の重み
j = -m, ･･･, -1, 0, 1, ･･･, m
1次: 単純移動平均
2次と3次は同じ重みになる
2次および3次多項式適合法の重み

## Slide 7: 最適条件として、3次、31点を選んだ

## Slide 8: plot

## Slide 9: 微分

## Slide 10: 31点、51点で1次微分

## Slide 11: 31点、51点で2次微分

## Slide 12: 補足資料

## Slide 13: Smoothing (平滑化)
Take some average for sample points ・ Moving average (移動平均)
・ Simple moving average (単純移動平均): Average of sequential data with the uniform weight ・Weighted moving average (加重移動平均): Average of sequential data with weight Weight： Linear, Triangular, Exponetnial, Gauss, etc…
Approximate sample points by some function ・ Polynomial smoothing (多項式による平滑化) ・ Smoothing spline (スプライン平滑化)
・ Least-squares method (最小二乗法)
Other
・ Fourier transformation (フーリエ変換)

## Slide 14: Calculation
Simple moving average (2m+1 points)
Weighted moving average (2m+1 points)

## Slide 15: Smoothing (平滑化)
・ Moving average (移動平均法) Smoother with more sample points for average, but would alter the function shape if the function is not monotonic. => Affect peak height, valley depth, peak width etc…
The range of averaged sample points larger than the peak width => split peaks might become difficult to be separated.
Poor S/N ratio XRD pattern
・ sample points
Red: 5-points simple moving average
Simple moving average: 5,11,31点

## Slide 16: Smoothing: Polynomial fit method (多項式適合法)
Simple moving average: 5, 11, 31 points
Polynomial fit: 11, 31 points
Adopt norder order polynomial to ns sample points among the given n sample points, determined by LSQ
データに norder次多項式を最小自乗法で求め、標本点の値を内挿する

## Slide 17: Weights of polynomial fit (Savizky-Golay method) 多項式適合法 (Savizky-Golay法) の重み
南茂夫, 科学計測のための波形データ処理, CQ出版社 (1986)
Weights for order 2 and 3 using (2m+1) points ((2m+1)点を用いた2,3次多項式適合の重み)
j = -m, ･･･, -1, 0, 1, ･･･, m
Order 1: Simple moving average
Orders 2 and 3 have the same weights
Table 5.1 Weights for order 2 and 3 polynomial fit

## Slide 18: Calculation
Simple moving average (2m+1 points)
Weighted moving average (2m+1 points)
Order 2 and 3 polynomial fit using (2m+1) points
j = -m, ･･･, -1, 0, 1, ･･･, m

## Slide 19: Smoothing
Simple moving average (2m+1 points)
Weight

## Slide 20
Weighted moving average (2m+1 points)
wi
Smoothing

## Slide 21
Order 2 and 3 polynomial fit using (2m+1) points
j = -m, ･･･, -1, 0, 1, ･･･, m
w23(j)
Smoothing

## Slide 22: Filter and convolution
First differential
Second differential
Simple moving average (3 points)
Weighted moving average (3p one-side triangle)
Weighted moving average (3p double-side triangle)
Polynomial fit smoothing (2m+1 points)
Differentiation, smoothing, convolution may be performed with the same convolution program by adopting appropriate filters. 微分、平滑化、コンボリューションは、 フィルターを変えるだけで 同じコンボリューションプログラムを流用できる
Filter
Convolution: Matrix product of data vector and filter

## Slide 23: Weights for various smoothing
Equivalent to convolution using these functions
Weighted moving average (2m+1 points)
e.g., one-side triangle :
triangle :
Gaussian :

## Slide 24: Weights
Order 2 and 3 polynomial fit using (2m+1) points
Equivalent to convolution using these functions

## Slide 25: Smoothing by python library
Simple moving average
# make a constant filter with weight of 1/N
w = np.ones(nsmooth) / nsmooth
# convolution
ys = np.convolve(y, w, mode = ‘same‘)
Polynomial smoothing: Savizky-Golay filter
ys = scipy.signal.savgol_filter(y, nsmooth, norder, deriv = 0) nsmooth: number of smoothing points
norder : order of polynomial
deriv : order of differentiation
注意: savgol_filter() takes differentiation to specify deriv = 1, but its absolute values are different from the first differentials
because savgol_filter() does not know x-axis values. Divide the results by hderiv after smoothing if you need absolute values Note: check the final results by yourself

## Slide 26: Multi-dimensional filter, convolution, image processing
filter:
X differential filter (edge detection)
Y differential filter (edge detection)
Diagonal differential filter (edge detection)
Smoothing filter (smearing/blur)  sharpening can be done by deconvolution
Convoluted Neural Network (畳み込みニューラルネットワーク)
Insert a convolution layer in multilayer neural network to learn the elements of the filter
We may know how the filter works by analyzing the values of the filter elements
e.g., the convolution of y22 is given by
a sum of each product of data and filter
NOTE: different from convolution in mathematics